## Slide 1
CAPSTONE FIRST DRAFT / ZEROTH REVIEW • GROUP 1
Thermal-Aware Power Budgeting on a Silicon Die
Problem A | PDEs, Transforms & Optimization | S3 EC | Team of 5
PROBLEM SCOPE
DOMAIN 10 mm × 10 mm silicon die; k = 150 W/(m·K); 40 × 40 mesh.
CORES 4 active nodes: (10,10), (10,29), (29,10), (29,29).
BOUNDARY Dirichlet heat-sink boundary: T_amb = 300 K on all edges.
OBJECTIVE Choose q = [q₁,q₂,q₃,q₄] to minimize peak chip temperature.
TEAM
Aarsha B Lekshmi • Ajil Reji • Anagh Prasad • Ashwin Nelson • Denin Thomas Jacob
150 W/(m·K)
Silicon thermal conductivity
ΔT ≥ 5 K
Target hotspot reduction 343 K uniform → ~327 K LP-optimal
5 W
Total power budget ceiling P_max over 4 cores
q = [q₁, q₂, q₃, q₄] | Σqᵢ ≤ 5 W
Saintgits College of Engineering • October 2026
1 / 4

## Slide 2
Six Modules, One Chain, Five Owners
The mathematical pipeline is split into six explicit handoff modules.
M1
Field model
Vector Calculus
Aarsha B Lekshmi | Vector Calculus (S2)
Fourier: q = −k∇T Energy balance: ∇·q = Q
M2
PDE formulation
PDEs
Aarsha B Lekshmi | PDEs (S3)
∇²T = −Q/k T = 300 K on all edges
M3
Transform solution
Laplace Transforms
Ajil Reji | Laplace Transforms (S3)
Z_th(s) = ΔT(s)/P(s) DC limit s → 0 → thermal resistance
M4
Discretization
Linear Algebra
Anagh Prasad | Linear Algebra (S1)
40×40 mesh → 5-point FDM Sparse system A T = q
M5
LP power allocation
Linear Programming
Ashwin Nelson | Optimization (S3)
min t s.t. A T = q; Tᵢ ≤ t; Σqᵢ ≤ P_max; q ≥ 0
M6
Pipeline + verification
Python Lab
Denin Thomas Jacob | Python Lab (S3)
Sparse solve + linprog Heatmaps, bar charts, run.py
HANDOFF CHAIN
A (PDE, BCs) → B (Z_th check) → C (Sparse matrix A) → D (q*, T*) → E (figures & run.py)
The LP follows from the discretized physical heat equation; it is not a bolt-on heuristic. Git: feature branches → main.
PDEs, Transforms & Optimization Techniques | Problem A
2 / 4

## Slide 3
Mathematical Backbone & Verification Criteria
STAGE
COURSE
GOVERNING EQUATIONS
IMPLEMENTATION / VERIFICATION
Field Model
Vector Calculus
q = −k∇T; ∇·q = Q
Continuous heat-flux field through bulk silicon.
PDEs
PDEs
∇²T(x,y) = −Q(x,y)/k; T = 300 K on ∂Ω
2D elliptic boundary-value problem.
Transform
Laplace
ρcₚsT(s) = k∇²T(s) + Q(s); Z_th(s)=ΔT(s)/P(s)
DC limit s→0 checks steady-state thermal resistance.
Discretization
Linear Algebra
(Tᵢ₊₁ⱼ−2Tᵢⱼ+Tᵢ₋₁ⱼ)/h² + (Tᵢⱼ₊₁−2Tᵢⱼ+Tᵢⱼ₋₁)/h² = −Qᵢⱼ/k; A T=q
40×40 grid; sparse 5-point stencil / CSR.
LP Allocation
Optimization
min t s.t. A T=q; Tᵢ≤t; Σqᵢ≤5 W; qᵢ≥0
Epigraph LP solved with scipy.optimize.linprog / HiGHS.
VERIFICATION
Edges remain exactly 300 K • max(λ(A_int)) < 0 • Σqᵢ = 5 W • Peak ≈ 343 K uniform → ≈327 K optimal • target drop ≥ 5 K
PDEs, Transforms & Optimization Techniques | Problem A
3 / 4

## Slide 4
Tools, Outcomes, Risks & 6-Day Execution Plan
PYTHON STACK & TOOLS
• NumPy — grid coordinates, indexing and array slicing.
• SciPy — CSR sparse assembly + scipy.optimize.linprog (HiGHS).
• SymPy — symbolic Laplace transform and s → 0 limits.
• Matplotlib / Seaborn — thermal maps, allocation bars, P_max sweeps.
• Git — python run.py regenerates the full figure set in < 2 min.
EXPECTED OUTCOMES
• Uniform vs. LP-optimal thermal heatmaps.
• Power shifted toward better cooling paths.
• Peak hotspot reduction ≥ 5 K: ~343 K → ~327 K.
• linprog returns res.success == True.
• Σ qᵢ ≤ 5.0 W with qᵢ ≥ 0.
RISKS & MITIGATIONS
• Ill-conditioning → direct sparse solve / preconditioning fallback.
• Boundary leakage → automated assertions: every edge T == 300 K.
• LP infeasibility / solver issue → explicit q ≥ 0 bounds + HiGHS.
• Interface drift → fixed stage contracts + daily Git merges.
SIX-DAY EXECUTION
• DAY 1 — Stages 1–3 derivation + Git initialization.
• DAY 2 — 40×40 FDM matrix, CSR assembly, eigenvalue check.
• DAY 3 — Epigraph LP + linprog tests.
• DAY 4 — End-to-end heatmaps + P_max sweep.
• DAY 5 — 6-page IEEE report + sanity checklist.
• DAY 6 — Clean-machine run.py test + 10-min rehearsal + submission.
DELIVERABLES | 6-page IEEE report • Reproducible Git repository • Live 10-minute demo • Signed pipeline table
PDEs, Transforms & Optimization Techniques | Problem A
4 / 4